## Slide 1: Big Data and Geospatial Analysis in Agriculture and Environment
Takaaki Masaki
Revocatus Paul

## Slide 2: Overview of the workshop
Date | Theme
Day 1 (April 22) | Introduction to Big Data, GIS, and R programming
Day 2 (April 23) | Advanced topics in GIS
Day 3 (April 24) | Introduction to Geospatial Data on Environment and Agriculture
Day 4 (April 25) | Integrating Survey Data with Geospatial Data
Day 5 (April 26) | Group study proposal presentation
Day 6 (April 29) | Introduction to GitHub and Google Earth Engine
Day 7 (April 30) | Group study presentation

## Slide 3
https://github.com/takaakimasaki/tanzania_spatial_training_2024
Overview of the workshop

## Slide 4: Brief introduction
Name
Organization
Reasons for taking this course
Any topics that you would like us to cover during the workshop?

## Slide 5: day 1: Introduction to Big Data, GIS, and R programming
Takaaki Masaki
Revocatus Paul

## Slide 6: What is big data?
Big Data is defined by volume, velocity and variety — large amounts of data coming in quickly in a number of formats.
Geospatial data is a crucial component of big data, adding context that allows for better, multidimensional insights that facilitate smarter decisions, improved business operations and innovation to deliver a strong competitive advantage.

## Slide 7: Agricultural and environmental statistics through the lens of big data
“Geospatial information adds significant value and utility to environment statistics. Ideally, geographic aspects of data should always be collected, represented and analysed at the most detailed scale possible, based on national capacities and priorities” (FDES 2013)
Notes: https://unstats.un.org/unsd/environment/FDES/FDES-2015-supporting-tools/FDES.pdf

## Slide 8
Table: Main attributes of the components of the FDES
Notes: https://unstats.un.org/unsd/environment/FDES/FDES-2015-supporting-tools/FDES.pdf

## Slide 9: There is so much geospatial data out there!
Google Earth Engine (GEE) has over 50 petabytes of data, including 900 datasets and over 30 years of historical imagery (1P = 1000T = 1,000,000 GB)

## Slide 10: Example 1: ESRI Land Cover

## Slide 11: Example 2: GAEZ Version 4

## Slide 12: Example 3: SPEI Global Drought Monitor

## Slide 13: Monitoring drought in Tanzania through the Agricultural Stress Index (ASI)
The ASI is a quick-look indicator that facilitates the early identification of cropped land with a high likelihood of water stress (drought).

## Slide 14: GIS and Spatial Analysis

## Slide 15: Different types of spatial data

## Slide 16: Different types of spatial data
Examples:
Schools
Hospitals
Roads
Railway
Country/region/district boundary
Population density
Rainfall
Temperature

## Slide 17: GIS file formats

## Slide 18: GIS file formats
File formats | Shapefile | netCDF & GEOTIFF
Data Types | Point & Line & Polygon | Raster

## Slide 19: Shapefile
A shapefile is a vector data format that stores the location, geometry, and attributes of geographic features, such as points, lines, and polygons.
Let’s say you would like to generate a map of Tanzania
    Download the shapefile of administrative boundary from HDX
  You will see a list of various files that make up a shapefile, including SHP, SHX, DBF, PRJ, XML, SBN, SBX, and CPG.
    SHP is a mandatory Esri file that gives features their geometry.
    SHX are mandatory Esri and AutoCAD shape index positions. This type of file is used to search forward and backward.
    DBF is a standard database file used to store attribute data and object IDs.
    PRJ is an optional file that contains the metadata associated with the shapefiles coordinate and projection system.
  See more details on this topic on the ESRI website

## Slide 20: Example: raster data (GEOTIFF, TIFF, netCDF)
Raster data comes in the form of GEOTIFF, TIFF, or netCDF
TIFF: Adobe Tagged Image File Format (TIFF or TIF, same thing) is so universally used as a format for imagery. TIF files can contain tags, additional items of information, that can be used to extend the standard for different purposes
GEOTIFF: A GeoTIFF is a TIF file that ends in a three letter . tif extension just like other TIF files, but a GeoTIFF contains additional tags that provide projection information for that image as specified by the GeoTIFF standard.
netCDF: Network Common Data Form (netCDF) is a file format for storing multidimensional scientific data (variables) such as temperature, humidity, pressure, wind speed, and direction

## Slide 21: Examples of vector/raster datasets in different formats: 1-lecture_code.R

## Slide 22: Coordinate systems

## Slide 23: Coordinate systems
https://www.youtube.com/watch?v=Z41Dt7_R180

## Slide 24: Coordinate systems
Shape: Spherical
Unit: Degree (Longitude & Latitude)
Example: WGS84 (EPSG:4326)
Shape: Flat
Unit: Meter (X & Y)
Example: Pseudo-Mercator (EPSG:3857)
Geographic Coordinate System
Projected Coordinate System
There are many coordinate reference systems (CRS) (i.e., standards for describing locations) based on the two systems above.
So, it’s important to check coordinate reference systems before analysis.
Notes: See more on this: https://www.e-education.psu.edu/geog160/node/1918
See more on https://www.joaoleitao.com/different-world-map-projections/

## Slide 25: Getting projection right

## Slide 26: GIS Analysis Software

## Slide 27: GIS Analysis Software
Python
- Programming language
- General purpose
- Open-source (free to use)
R
- Programming Language
- Focused on statistical analysis
- Open-source (Free to use)
ArcGIS
- Software
- Built for GIS analysis
- Proprietary software (NOT free to use)
QGIS
- Software
- Built for GIS analysis
- Open-source (free to use)

## Slide 28: Introduction to R programming

## Slide 29: How to install R and RStudio
Go to https://cran.r-project.org/
Download the latest version of R for your computer
Go to https://www.rstudio.com/products/rstudio/download/#download
Download the latest version of R for your computer
1. Install R
2. Install RStudio

## Slide 30: Basic user interface of RStudio
Source
Console/ Terminal
Environment/
History
Files/Plots/ Packages/Help
This is where you code
This is where your code is evaluated by R
This is where you can see variables and command history
This is where you can check files, plots, packages and help from R

## Slide 31: 1_handson.R
Hands-on exercise
In this exercise, you will learn:
  Basics in R programming
  How to read shapefile and raster files
  How to manipulate these datasets (using dplyr package)
  Generate basic maps (using plot function)

## Slide 32
Q&A